## Slide 1: Prelab 4

## Slide 2: Assembler
Assembly
Code
Assembler
Pre-processing
(part 1)
Convert to Binary
(part 2)
CPU
Machine
Code
(Binary)

## Slide 3: Assembler
Assembly
Code
filename.asm
Assembler
Pre-processing
(part 1)
Convert to Binary
(part 2)
CPU
Machine
Code
(Binary) filename_out2.bin
Pre-processed Assembly Code filename_out1.txt

## Slide 4: Input/Output Files
INST ARG1 ARG2 ARG3
lw 7 9 0
addi 10 0 10
addi 11 0 20
bge 10 11 12
add 12 11 0
jal 1 12
add 12 10 0
jal 1 4
sw 9 10 0
example1_out1.txt
Machine Code (Binary)
00000000000001001000001110000011
00000000101000000000010100010011
00000001010000000000010110010011
00000000101101010101001101100011
00000000000001011000011000110011
00000000000000000110000011101111
00000000000001010000011000110011
00000000000000000010000011101111
00000000101001001010000000100011
example1_out2.bin
Assemble (part 2)

## Slide 5: RV32IM – List of Instructions
RISC-V ISA for RV32IM – Modified |  |  |  |  |  |  | 
Format | Name | Instruction | Operands | Meaning | Opcode | Funct3 | Funct7
R-type | Addition | add | rd, rs1, rs2 | rd = rs1 + rs2 | 0110011 | 000 | 0000000
 | Subtraction | sub | rd, rs1, rs2 | rd = rs1 - rs2 | 0110011 | 000 | 0100000
 | Multiplication | mul | rd, rs1, rs2 | rd = rs1 * rs2 | 0110011 | 000 | 0000001
 | Division | div | rd, rs1, rs2 | rd = rs1 / rs2 | 0110011 | 100 | 0000001
 | Logic left shift | sll | rd, rs1, rs2 | rd = rs1 << rs2 | 0110011 | 001 | 0000000
 | Logic right shift | srl | rd, rs1, rs2 | rd = rs1 >> rs2 | 0110011 | 101 | 0000000
 | Arithmetic right shift | sra | rd, rs1, rs2 | rd = rs1 >>> rs2 | 0110011 | 011 | 0000001
 | Bitwise OR | or | rd, rs1, rs2 | rd = rs1 ¦ rs2 | 0110011 | 110 | 0000000
 | Bitwise AND | and | rd, rs1, rs2 | rd = rs1 & rs2 | 0110011 | 111 | 0000000
 | Birwise XOR | xor | rd, rs1, rs2 | rd = rs1 ^ rs2 | 0110011 | 100 | 0000000
I-type | Load word (32-bits) | lw | rd, imm(rs1) | rd = M[rs1 + imm] | 0000011 | 000 | n.a.
 | Add immediate | addi | rd, rs1, imm | rd = rs1 + imm | 0010011 | 000 | n.a.
 | Logic left shift immediate | slli | rd, rs1, imm | rd = rs1 << imm | 0010011 | 001 | n.a.
 | Logic right shift immediate | srli | rd, rs1, imm | rd = rs1 >> imm | 0010011 | 101 | n.a.
 | Arithmetic right shift immediate | srai | rd, rs1, imm | rd = rs1 >>> imm | 0010011 | 011 | n.a.
 | Bitwise OR immediate | ori | rd, rs1, imm | rd = rs1 ¦ imm | 0010011 | 110 | n.a.
 | Bitwise AND immediate | andi | rd, rs1, imm | rd = rs1 & imm | 0010011 | 111 | n.a.
 | Birwise XOR immediate | xori | rd, rs1, imm | rd = rs1 ^ imm | 0010011 | 100 | n.a.
 | Jump & link register | jalr | rd, rs1, imm | rd=PC+4; PC=rs1 + imm | 1100111 | 000 | n.a.
S-type | Store word (32-bits) | sw | rs2, imm(rs1) | M[rs1 + imm] = rs2 | 0100011 | 010 | n.a.
B-type | Branch if equal | beq | rs1, rs2, imm | if(rs1 == rs2): PC += imm | 1100011 | 000 | n.a.
 | Branch if not equal | bne | rs1, rs2, imm | if(rs1 != rs2): PC += imm | 1100011 | 001 | n.a.
 | Branch if less than | blt | rs1, rs2, imm | if(rs1 < rs2): PC += imm | 1100011 | 100 | n.a.
 | Branch if greater or equal | bge | rs1, rs2, imm | if(rs1 >= rs2): PC += imm | 1100011 | 101 | n.a.
J-type | Jump & link | jal | rd, imm | rd=PC+4; PC += imm | 1101111 | n.a. | n.a.
RV32IM – Table.xlsx (tab: “ISA”)

## Slide 6: Machine Instructions’ Format
RISC-V Instructions Format for RV32IM – Modified |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Field |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Comments
Bits | Size | 7 bits |  |  |  |  |  |  | 5 bits |  |  |  |  | 5 bits |  |  |  |  | 3 bits |  |  | 5 bits |  |  |  |  | 7 bits |  |  |  |  |  |  | 
 | Range | 31 |  |  |  |  |  | 25 | 24 |  |  |  | 20 | 19 |  |  |  | 15 | 14 |  | 12 | 11 |  |  |  | 7 | 6 |  |  |  |  |  | 0 | 
Format | R-type | funct7 |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  |  |  | Reg-reg arithmetic
 | I-type | imm[11:0] |  |  |  |  |  |  |  |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  |  |  | Load & reg-immediate arithmetic
 | S-type | imm[11:5] |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | imm[4:0] |  |  |  |  | opcode |  |  |  |  |  |  | Store
 | B-type | imm[12:6] |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | imm[5:1] |  |  |  |  | opcode |  |  |  |  |  |  | Conditional branch format
 | J-type | imm[20:1] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | rd |  |  |  |  | opcode |  |  |  |  |  |  | Unconditional jump format
RV32IM – Table.xlsx (tab: “Format”)

## Slide 7: Example: R-Types
RISC-V Instructions Format for RV32IM – Modified |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Field |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Comments
Bits | Size | 7 bits |  |  |  |  |  |  | 5 bits |  |  |  |  | 5 bits |  |  |  |  | 3 bits |  |  | 5 bits |  |  |  |  | 7 bits |  |  |  |  |  |  | 
 | Range | 31 |  |  |  |  |  | 25 | 24 |  |  |  | 20 | 19 |  |  |  | 15 | 14 |  | 12 | 11 |  |  |  | 7 | 6 |  |  |  |  |  | 0 | 
Format | R-type | funct7 |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  |  |  | Reg-reg arithmetic
INST rd rs1 rs2
add 12 11 0
example1_out1.txt
RISC-V ISA for RV32IM – Modified |  |  |  |  |  |  | 
Format | Name | Instruction | Operands | Meaning | Opcode | Funct3 | Funct7
R-type | Addition | add | rd, rs1, rs2 | rd = rs1 + rs2 | 0110011 | 000 | 0000000

## Slide 8: Example: R-Types
RISC-V Instructions Format for RV32IM – Modified |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Field |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Comments
Bits | Size | 7 bits |  |  |  |  |  |  | 5 bits |  |  |  |  | 5 bits |  |  |  |  | 3 bits |  |  | 5 bits |  |  |  |  | 7 bits |  |  |  |  |  |  | 
 | Range | 31 |  |  |  |  |  | 25 | 24 |  |  |  | 20 | 19 |  |  |  | 15 | 14 |  | 12 | 11 |  |  |  | 7 | 6 |  |  |  |  |  | 0 | 
Format | R-type | funct7 |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  |  |  | Reg-reg arithmetic
INST rd rs1 rs2
add 12 11 0
example1_out1.txt
INST rd rs1 rs2
add 01100 01011 00000
RISC-V ISA for RV32IM – Modified |  |  |  |  |  |  | 
Format | Name | Instruction | Operands | Meaning | Opcode | Funct3 | Funct7
R-type | Addition | add | rd, rs1, rs2 | rd = rs1 + rs2 | 0110011 | 000 | 0000000
Convert to Binary

## Slide 9: Example: R-Types
RISC-V Instructions Format for RV32IM – Modified |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Field |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Comments
Bits | Size | 7 bits |  |  |  |  |  |  | 5 bits |  |  |  |  | 5 bits |  |  |  |  | 3 bits |  |  | 5 bits |  |  |  |  | 7 bits |  |  |  |  |  |  | 
 | Range | 31 |  |  |  |  |  | 25 | 24 |  |  |  | 20 | 19 |  |  |  | 15 | 14 |  | 12 | 11 |  |  |  | 7 | 6 |  |  |  |  |  | 0 | 
Format | R-type | funct7 |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  |  |  | Reg-reg arithmetic
INST rd rs1 rs2
add 12 11 0
example1_out1.txt
INST rd rs1 rs2
add 01100 01011 00000
funct3 rs2 rs1 funct3 rd opcode
0000000 00000 01011 000 01100 0110011
example1_out2.bin
RISC-V ISA for RV32IM – Modified |  |  |  |  |  |  | 
Format | Name | Instruction | Operands | Meaning | Opcode | Funct3 | Funct7
R-type | Addition | add | rd, rs1, rs2 | rd = rs1 + rs2 | 0110011 | 000 | 0000000
Convert to Binary
Get fields & assemble

## Slide 10: Example: I-Types
RISC-V Instructions Format for RV32IM – Modified |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Field |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Comments
Bits | Size | 7 bits |  |  |  |  |  |  | 5 bits |  |  |  |  | 5 bits |  |  |  |  | 3 bits |  |  | 5 bits |  |  |  |  | 7 bits |  |  |  |  |  |  | 
 | Range | 31 |  |  |  |  |  | 25 | 24 |  |  |  | 20 | 19 |  |  |  | 15 | 14 |  | 12 | 11 |  |  |  | 7 | 6 |  |  |  |  |  | 0 | 
Format | I-type | Imm[11:0] |  |  |  |  |  |  |  |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  |  |  | Load & reg-immediate arithmetic
INST rd rs1 imm
addi 10 0 10
example1_out1.txt
RISC-V ISA for RV32IM – Modified |  |  |  |  |  |  | 
Format | Name | Instruction | Operands | Meaning | Opcode | Funct3 | Funct7
I-type | Add immediate | addi | rd, rs1, imm | rd = rs1 + imm | 0010011 | 000 | n.a.

## Slide 11: Example: I-Types
RISC-V Instructions Format for RV32IM – Modified |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Field |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Comments
Bits | Size | 7 bits |  |  |  |  |  |  | 5 bits |  |  |  |  | 5 bits |  |  |  |  | 3 bits |  |  | 5 bits |  |  |  |  | 7 bits |  |  |  |  |  |  | 
 | Range | 31 |  |  |  |  |  | 25 | 24 |  |  |  | 20 | 19 |  |  |  | 15 | 14 |  | 12 | 11 |  |  |  | 7 | 6 |  |  |  |  |  | 0 | 
Format | I-type | Imm[11:0] |  |  |  |  |  |  |  |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  |  |  | Load & reg-immediate arithmetic
INST rd rs1 imm
addi 10 0 10
example1_out1.txt
RISC-V ISA for RV32IM – Modified |  |  |  |  |  |  | 
Format | Name | Instruction | Operands | Meaning | Opcode | Funct3 | Funct7
I-type | Add immediate | addi | rd, rs1, imm | rd = rs1 + imm | 0010011 | 000 | n.a.
INST rd rs1 imm[11:0]
addi 01010 00000 000000001010
Convert to Binary

## Slide 12: Example: I-Types
RISC-V Instructions Format for RV32IM – Modified |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Field |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Comments
Bits | Size | 7 bits |  |  |  |  |  |  | 5 bits |  |  |  |  | 5 bits |  |  |  |  | 3 bits |  |  | 5 bits |  |  |  |  | 7 bits |  |  |  |  |  |  | 
 | Range | 31 |  |  |  |  |  | 25 | 24 |  |  |  | 20 | 19 |  |  |  | 15 | 14 |  | 12 | 11 |  |  |  | 7 | 6 |  |  |  |  |  | 0 | 
Format | I-type | Imm[11:0] |  |  |  |  |  |  |  |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  |  |  | Load & reg-immediate arithmetic
INST rd rs1 imm
addi 10 0 10
example1_out1.txt
RISC-V ISA for RV32IM – Modified |  |  |  |  |  |  | 
Format | Name | Instruction | Operands | Meaning | Opcode | Funct3 | Funct7
I-type | Add immediate | addi | rd, rs1, imm | rd = rs1 + imm | 0010011 | 000 | n.a.
INST rd rs1 imm[11:0]
addi 01010 00000 000000001010
example1_out2.bin
Convert to Binary
imm[11:0] rs1 funct3 rd opcode
000000001010 00000 000 01010 0010011
Get fields & assemble

## Slide 13: Example: B-Types
RISC-V Instructions Format for RV32IM – Modified |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Field |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Comments
Bits | Size | 7 bits |  |  |  |  |  |  | 5 bits |  |  |  |  | 5 bits |  |  |  |  | 3 bits |  |  | 5 bits |  |  |  |  | 7 bits |  |  |  |  |  |  | 
 | Range | 31 |  |  |  |  |  | 25 | 24 |  |  |  | 20 | 19 |  |  |  | 15 | 14 |  | 12 | 11 |  |  |  | 7 | 6 |  |  |  |  |  | 0 | 
Format | B-type | imm[12:6] |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | imm[5:1] |  |  |  |  | opcode |  |  |  |  |  |  | Conditional branch format
INST rd rs1 imm
bge 10 11 12
example1_out1.txt
RISC-V ISA for RV32IM – Modified |  |  |  |  |  |  | 
Format | Name | Instruction | Operands | Meaning | Opcode | Funct3 | Funct7
B-type | Branch if not equal | bne | rs1, rs2, imm | if(rs1 != rs2): PC += imm | 1100011 | 001 | n.a.

## Slide 14: Example: B-Types
RISC-V Instructions Format for RV32IM – Modified |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Field |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Comments
Bits | Size | 7 bits |  |  |  |  |  |  | 5 bits |  |  |  |  | 5 bits |  |  |  |  | 3 bits |  |  | 5 bits |  |  |  |  | 7 bits |  |  |  |  |  |  | 
 | Range | 31 |  |  |  |  |  | 25 | 24 |  |  |  | 20 | 19 |  |  |  | 15 | 14 |  | 12 | 11 |  |  |  | 7 | 6 |  |  |  |  |  | 0 | 
Format | B-type | imm[12:6] |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | imm[5:1] |  |  |  |  | opcode |  |  |  |  |  |  | Conditional branch format
INST rd rs1 imm
bge 10 11 12
example1_out1.txt
RISC-V ISA for RV32IM – Modified |  |  |  |  |  |  | 
Format | Name | Instruction | Operands | Meaning | Opcode | Funct3 | Funct7
B-type | Branch if not equal | bne | rs1, rs2, imm | if(rs1 != rs2): PC += imm | 1100011 | 001 | n.a.
INST rd rs1 imm[12:0]
addi 01010 00000 0000000001100
Convert to Binary

## Slide 15: Example: B-Types
RISC-V Instructions Format for RV32IM – Modified |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Field |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Comments
Bits | Size | 7 bits |  |  |  |  |  |  | 5 bits |  |  |  |  | 5 bits |  |  |  |  | 3 bits |  |  | 5 bits |  |  |  |  | 7 bits |  |  |  |  |  |  | 
 | Range | 31 |  |  |  |  |  | 25 | 24 |  |  |  | 20 | 19 |  |  |  | 15 | 14 |  | 12 | 11 |  |  |  | 7 | 6 |  |  |  |  |  | 0 | 
Format | B-type | imm[12:6] |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | imm[5:1] |  |  |  |  | opcode |  |  |  |  |  |  | Conditional branch format
INST rd rs1 imm
bge 10 11 12
example1_out1.txt
RISC-V ISA for RV32IM – Modified |  |  |  |  |  |  | 
Format | Name | Instruction | Operands | Meaning | Opcode | Funct3 | Funct7
B-type | Branch if not equal | bne | rs1, rs2, imm | if(rs1 != rs2): PC += imm | 1100011 | 001 | n.a.
INST rd rs1 imm[12:0]
addi 01010 00000 0000000001100
example1_out2.bin
Convert to Binary
imm[12:6] rs2 rs1 funct3 imm[5:1] opcode
0000000 01011 01010 101 00110 1100011
Get fields & assemble

## Slide 16: Example: B-Types
RISC-V Instructions Format for RV32IM – Modified |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Field |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Comments
Bits | Size | 7 bits |  |  |  |  |  |  | 5 bits |  |  |  |  | 5 bits |  |  |  |  | 3 bits |  |  | 5 bits |  |  |  |  | 7 bits |  |  |  |  |  |  | 
 | Range | 31 |  |  |  |  |  | 25 | 24 |  |  |  | 20 | 19 |  |  |  | 15 | 14 |  | 12 | 11 |  |  |  | 7 | 6 |  |  |  |  |  | 0 | 
Format | B-type | imm[12:6] |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | imm[5:1] |  |  |  |  | opcode |  |  |  |  |  |  | Conditional branch format
INST rd rs1 imm
bge 10 11 12
example1_out1.txt
RISC-V ISA for RV32IM – Modified |  |  |  |  |  |  | 
Format | Name | Instruction | Operands | Meaning | Opcode | Funct3 | Funct7
B-type | Branch if not equal | bne | rs1, rs2, imm | if(rs1 != rs2): PC += imm | 1100011 | 001 | n.a.
INST rd rs1 imm[12:0]
addi 01010 00000 0000000001100
example1_out2.bin
Convert to Binary
imm[0:6+1] rs2 rs1 funct3 imm[7:11+1] opcode
0000000 01011 01010 101 00110 1100011
Get fields & assemble
PYTHON: Reversed Indexing

## Slide 17: Machine Instructions’ Format
RISC-V Instructions Format for RV32IM – Modified |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Field |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Comments
Bits | Size | 7 bits |  |  |  |  |  |  | 5 bits |  |  |  |  | 5 bits |  |  |  |  | 3 bits |  |  | 5 bits |  |  |  |  | 7 bits |  |  |  |  |  |  | 
 | Range | 31 |  |  |  |  |  | 25 | 24 |  |  |  | 20 | 19 |  |  |  | 15 | 14 |  | 12 | 11 |  |  |  | 7 | 6 |  |  |  |  |  | 0 | 
Format | R-type | funct7 |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  |  |  | Reg-reg arithmetic
 | I-type | imm[11:0] |  |  |  |  |  |  |  |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  |  |  | Load & reg-immediate arithmetic
 | S-type | imm[11:5] |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | imm[4:0] |  |  |  |  | opcode |  |  |  |  |  |  | Store
 | B-type | imm[12:6] |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | imm[5:1] |  |  |  |  | opcode |  |  |  |  |  |  | Conditional branch format
 | J-type | imm[20:1] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | rd |  |  |  |  | opcode |  |  |  |  |  |  | Unconditional jump format
RV32IM – Table.xlsx (tab: “Format”)